## Slide 1: Register Transfer Operations
Register Transfer Operations – The movement and processing of data stored in registers
Three basic components:
  set of registers
  operations
  control of operations
Elementary Operations -- load, count, shift, add, bitwise "OR", etc.
  Elementary operations called microoperations

## Slide 2: Register Notation
Letters and numbers – denotes a register (ex. R2, PC, IR)
Parentheses ( ) – denotes a range of register bits (ex. R1(1), PC(7:0), PC(L))
Arrow () – denotes data transfer (ex. R1  R2, PC(L)  R0)
Comma – separates parallel operations
Brackets [ ] – Specifies a memory address (ex. R0  M[AR], R3  M[PC] )
R
7 6 5 4 3 2 1 0
15 8
7 0
15 0
PC(H)
PC(L)
R2

## Slide 3: Conditional Transfer
If (K1 =1) then (R2  R1) is shortened to
K1: (R2  R1)
where K1 is a control variable specifying a conditional execution of the microoperation.
R1
R2
K
1
Clock
Load
n
Clock
K1
Transfer Occurs Here
No Transfers Occur Here

## Slide 4: Microoperations
Logical Groupings:
  Transfer - move data from one register to another
  Arithmetic - perform arithmetic on data in registers
  Logic - manipulate data or use bitwise logical operations
  Shift - shift data in registers
Arithmetic operations + Addition – Subtraction * Multiplication / Division
Logical operations  Logical OR  Logical AND  Logical Exclusive OR  Not

## Slide 5: Example Microoperations
Add the content of R1 to the content of R2 and place the result in R1.
R1 R1 + R2
Multiply the content of R1 by the content of R6 and place the result in PC.
PC  R1 * R6
Exclusive OR the content of R1 with the content of R2 and place the result in R1.
R1  R1  R2

## Slide 6: Example Microoperations (Continued)
Take the 1's Complement of the contents of R2 and place it in the PC.
PC  R2
On condition K1 OR K2, the content of R1 is Logic bitwise Ored with the content of R3 and the result placed in R1.
(K1 + K2): R1  R1  R3
NOTE: "+" (as in K1 + K2) and means “OR.” In R1  R1 + R3, + means “plus.”

## Slide 7: Control Expressions
The control expression for an operation appears to the left of the operation and is separated from it by a colon
Control expressions specify the logical condition for the operation to occur
Control expression values of:
  Logic "1" -- the operation occurs.
  Logic "0" -- the operation is does not occur.
Example: X K1 : R1  R1 + R2 X K1 : R1  R1 + R2 + 1
Variable K1 enables the add or subtract operation.
If X =0, then X =1 so X K1 = 1, activating the addition of R1 and R2.
If X = 1, then X K1 = 1, activating the addition of R1 and the two's complement of R2 (subtract).

## Slide 8: Arithmetic Microoperations
From Table 7-3:
Note that any register may be specified for source 1, source 2, or destination.
These simple microoperations operate on the whole word
Symbolic Designation
Description
R0
¬
R1 + R2
Addition
R0
¬
R1
Ones Complement
R0
¬
R1 + 1
Two's Complement
R0
¬
R2 +
R1 + 1
R2 minus R1 (2's Comp)
R1
¬
R1 + 1
Increment (count up)
R1
¬
R1
–
1
Decrement (count down)

## Slide 9: Logical Microoperations
From Table 7-4:
Symbolic
Designation
Description
R0
¬
R1
Bitwise NOT
R0
¬
R1
Ú
R2
Bitwise OR (sets bits)
R0
¬
R1
Ù
R2
Bitwise AND (clears bits)
R0
¬
R1
Å
R2
Bitwise EXOR (complements bits)

## Slide 10: Logical Microoperations (continued)
Let R1 = 10101010, and R2 = 11110000
Then after the operation, R0 becomes:

## Slide 11: Shift Microoperations
From Table 7-5:
Let R2 = 11001001
Then after the operation, R1 becomes:
Symbolic
Designation
Description
R1
¬
sl R2
Shift Left
R1
¬
sr R2
Shift Right
R1
Operation
10010010
R1
¬
sl R2
01100100
R1
¬
sr R2
Note: These shifts "zero fill". Sometimes a separate flip-flop is used to provide the data shifted in, or to “catch” the data shifted out.
Other shifts are possible (rotates, arithmetic) (see Chapter 10).

## Slide 12: Register Transfer Structures
Multiplexer-Based Transfers - Multiple inputs are selected by a multiplexer dedicated to the register
Bus-Based Transfers - Multiple inputs are selected by a shared multiplexer driving a bus that feeds inputs to multiple registers
Three-State Bus - Multiple inputs are selected by 3-state drivers with outputs connected to a bus that feeds multiple registers
Other Transfer Structures - Use multiple multiplexers, multiple buses, and combinations of all the above

## Slide 13: Multiplexer-Based Transfers
Multiplexers connected to register inputs produce flexible transfer structures (Note: Clocks are omitted for clarity)
The transfers are: K1: R0  R1 K2×K1: R0  R2
Load
R0
n
MUX
S
K
2
0
1
Load
Load
n
n
K
1
R2
R1

## Slide 14: Multiplexer and Bus-Based Transfers for Multiple Registers
Multiplexer dedicated to each register
Shared transfer paths for registers
  A shared transfer object is a called a bus (Plural: buses)
Bus implementation using:
  multiplexers
  three-state nodes and drivers
In most cases, the number of bits is the length of the receiving register

## Slide 15: Dedicated MUX-Based Transfers
Multiplexer connected to each register input produces a very flexible transfer structure =>
Characterize the simultaneous transfers possible with this structure.
S0
S1
S2
L0
L1
L2
n
n
MUX
S
0
1
n
R0
Load
n
n
MUX
S
0
1
n
R1
Load
n
n
MUX
S
0
1
n
R2
Load
Notes: There can be three distinct registers as source, so can simultaneously do any three register transfers
- totally flexible.

## Slide 16: Multiplexer Bus
A single bus driven by a multiplexer lowers cost, but limits the available transfers =>
Characterize the simultaneous transfers possible with this structure.
Characterize the cost savings compared to dedicated multiplexers
L0
n
n
MUX
S1 S0
0
1
n
2
S0
S1
L1
L2
n
R0
Load
n
R1
Load
n
R2
Load
n
Notes: Can have only one register as a source at a time. Thus a set of simultaneous transfers
can have only one register source. Could require up to three clock cycles if three different sources needed.
Costs:
Dedicated 18 gate inputs per bit plus 3 shared inverters with total of 3 inputs
Bus: 9 gate inputs per bit + shared decoder with 8 inputs
Bus clearly less costly.

## Slide 17: Three-State Bus
The 3-input MUX can be replaced by a 3-state node (bus) and 3-state buffers.
Cost is further reduced, but transfers are limited
Characterize the simultaneous transfers possible with this structure.
Characterize the cost savings and compare
Other advantages?
n
L0
L1
L2
n
R0
Load
n
R1
Load
n
R2
Load
n
n
E2
E1
E0
Notes: Same simultaneous transfer capability as multiplexer bus
Cost: 3 gate inputs per three state driver = 9 gate inputs
If decoder desired, 8 shared gate inputs.
Clearly least costly.
The “bus” is unique in that it is “bidirectional.” This is a significant advantage
since it cuts connections between chips for bus paths to 1/2.

## Slide 18: Datapaths
Guiding principles for basic datapaths:
  The set of registers
    Collection of individual registers
    A set of registers with common access resources called a register file
    A combination of the above
  Microoperation implementation
    One or more shared resources for implementing microoperations
    Buses - shared transfer paths
    Arithmetic-Logic Unit (ALU) - shared resource for implementing arithmetic and logic microoperations
    Shifter - shared resource for implementing shift microoperations

## Slide 19: Datapath Example
Four parallel-load registers
Two mux-based register selectors
Register destination decoder
Mux B for external constant input
Buses A and B with external address and data outputs
ALU and Shifter with Mux F for output select
Mux D for external data input
Logic for generating status bits V, C, N, Z

## Slide 20: Datapath Example: Performing a Microoperation
Microoperation: R0 ← R1 + R2
Apply 01 to A select to place contents of R1 onto Bus A
Apply 10 to B select to place contents of R2 onto B data and apply 0 to MB select to place B data on Bus B
Apply 0010 to G select to perform addition G = Bus A + Bus B
Apply 0 to MF select and 0 to MD select to place the value of G onto BUS D
Apply 00 to Destination select to enable the Load input to R0
Apply 1 to Load Enable to force the Load input to R0 to 1 so that R0 is loaded on the clock pulse (not shown)
The overall microoperation requires 1 clock cycle

## Slide 21: Datapath Example: Key Control Actions for Microoperation Alternatives
Perform a shift microoperation – apply 1 to MF select
Use a constant in a micro- operation using Bus B – apply 1 to MB select
Provide an address and data for a memory or output write microoperation – apply 0 to Load enable to prevent register loading
Provide an address and obtain data for a memory or output read microoperation – apply 1 to MD select
For some of the above, other control signals become don't cares

## Slide 22: Arithmetic Logic Unit (ALU)
In this and the next section, we deal with detailed design of typical ALUs and shifters
Decompose the ALU into:
  An arithmetic circuit
  A logic circuit
  A selector to pick between the two circuits
Arithmetic circuit design
  Decompose the arithmetic circuit into:
    An n-bit parallel adder
    A block of logic that selects four choices for the B input to the adder
    See next slide for diagram

## Slide 23: Arithmetic Circuit Design (continued)
There are only four functions of B to select as Y in G = A + Y:
  0
  B
  B
  1
What functions are implemented with carry-in to the adder = 0? =1?
Cin = 0
Cin = 1
G = A
G = A + 1
G = A – 1
G = A + B
G = A
G = A + B
G = A + B + 1
G = A + B + 1

## Slide 24: Arithmetic Circuit Design (continued)
Adding selection codes to the functions of B:
The useful arithmetic functions are labeled in the table
Note that all four functions of B produce at least one useful function
+
+
+
+
+
+

## Slide 25: Logic Circuit
The text gives a circuit implemented using a multiplexer plus gates implementing: AND, OR, XOR and NOT
Here we custom design a circuit for bit Gi by beginning with a truth table organized as a K-map and assigning (S1, S0) codes to AND, OR, etc.
Gi = S0 Ai Bi + S1 Ai Bi + S0 Ai Bi + S1 S0 Ai
Gate input count for MUX solution > 29
Gate input count for above circuit < 20
Custom design better
S1S0 | AND | OR | XOR | NOT
AiBi | 0 0 | 0 1 | 1 1 | 1 0
0 0 | 0 | 0 | 0 | 1
0 1 | 0 | 1 | 1 | 1
1 1 | 1 | 1 | 0 | 0
1 0 | 0 | 1 | 1 | 0

## Slide 26: Arithmetic Logic Unit (ALU) (continued)
The next most significant select signals, S0 for the arithmetic circuit and S1 for the logic circuit, are wired together, completing the two select signals for the logic circuit.
The remaining S2 completes the three select signals for the arithmetic circuit.

## Slide 27: Combinational Shifter Parameters
Direction: Left, Right
Number of positions with examples:
  Single bit:
    1 position
    0 and 1 positions
  Multiple bit:
    1 to n – 1 positions
    0 to n – 1 positions
Filling of vacant positions
  Many options depending on instruction set
  Here, will provide input lines or zero fill

## Slide 28: 4-Bit Basic Left/Right Shifter
Serial Inputs:
  IR for right shift
  IL for left shift
Serial Outputs
  R for right shift (Same as MSB input)
  L for left shift (Same as LSB input)
Shift Functions: (S1, S0) = 00 Pass B unchanged 01 Right shift 10 Left shift 11 Unused
B
3
I
R
I
L
S
Serial
output L
Serial
output R
2
B
2
B
1
B
0
H
0
H
1
H
2
H
3
S
M
U
X
0
1
2
S
M
U
X
0
1
2
S
M
U
X
0
1
2
S
M
U
X
0
1
2

## Slide 29: Barrel Shifter
A rotate is a shift in which the bits shifted out are inserted into the positions vacated
The circuit rotates its contents left from 0 to 3 positions depending on S: S = 00 position unchanged S = 10 rotate left by 2 positions S = 01 rotate left by 1 positions S = 11 rotate left by 3 positions
See Table 10-3 in text for details
D
3
S
0
3
S
1
S
0
M
U
X
D
2
D
1
D
0
Y
0
Y
1
Y
2
Y
3
S
1
0
1
2
3
S
1
S
0
M
U
X
0
1
2
3
S
1
S
0
M
U
X
0
1
2
3
S
1
S
0
M
U
X
0
1
2

## Slide 30: Barrel Shifter (continued)
Large barrel shifters can be constructed by using:
  Layers of multiplexers - Example 64-bit:
    Layer 1 shifts by 0, 16, 32, 48
    Layer 2 shifts by 0, 4, 8, 12
    Layer 3 shifts by 0, 1, 2, 3
    See example in section 12-2 of the text
  2 - dimensional array circuits designed at the electronic level

## Slide 31: Datapath Representation
Have looked at detailed design of ALU and shifter in the datapath in slide 8
Here we move up one level in the hierarchy from that datapath
The registers, and the multiplexer, decoder, and enable hardware for accessing them become a register file
The ALU, shifter, Mux F and status hardware become a function unit
The remaining muxes and buses which handle data transfers are at the new level of the hierarchy
Address out
Data out
Constant in
MB select
Bus A
Bus B
FS
V
C
N
Z
MD select
n
D data
Write
D address
A address
B address
A data
B data
2
m
x
n
Register file
m
m
m
n
n
n
n
n
A
B
Function
unit
F
4
MUX B
1
0
MUX D
0
1
n
n
Data in

## Slide 32: Datapath Representation (continued)
In the register file:
  Multiplexer select inputs become A address and B address
  Decoder input becomes D address
  Multiplexer outputs become A data and B data
  Input data to the registers becomes D data
  Load enable becomes write
The register file now appears like a memory based on clocked flip-flops (the clock is not shown)
The function unit labeling is quite straightforward except for FS
Address out
Data out
Constant in
MB select
Bus A
Bus B
FS
V
C
N
Z
MD select
n
D data
Write
D address
A address
B address
A data
B data
2
m
x
n
Register file
m
m
m
n
n
n
n
n
A
B
Function
unit
F
4
MUX B
1
0
MUX D
0
1
n
n
Data in

## Slide 33: The Control Word
The datapath has many control inputs
The signals driving these inputs can be defined and organized into a control word
To execute a microinstruction, we apply control word values for a clock cycle. For most microoperations, the positive edge of the clock cycle is needed to perform the register load
The datapath control word format and the field definitions are shown on the next slide

## Slide 34: The Control Word Fields
Fields
  DA – D Address
  AA – A Address
  BA – B Address
  MB – Mux B
  FS – Function Select
  MD – Mux D
  RW – Register Write
The connections to datapath are shown in the next slide
Control word
D
A
AA
BA
M
B
FS
M
D
R
W
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0

## Slide 35: Control Word Block Diagram
10
8
14
0
13
11
Bus D
Constant in
n
n
MUX B
1
0
D data
Write
D address
A address
B address
A data
B data
8
x
n
Register file
A
B
Function
unit
n
n
n
MUX D
0
1
n
n
Data in
Bus A
Bus B
R
W
12
AA
15
D
A
n
BA
9
Address out
Data out
V
C
N
Z
7
MD
1
MB
6
4
FS
5
3
2

## Slide 36: Control Word Encoding
F A
Encoding of Control
W
D
A
,
AA,
B
A
MB
FS
MD
R
W
Function
Code
Function
Code
Function
Code
Function
Code
Function
Code
R
0
000
Register
0
0000
Function
0
No write
0
R
1
001
Constant
1
0001
Data In
1
Write
1
R
2
010
0010
R
3
011
0011
R
4
100
0100
R
5
101
0101
R
6
110
0110
R
7
111
0111
1000
1001
1010
1011
1100
1101
1110
F
A
¬
F A
1
+
¬
B
¬
F A
B
1
¬
F A
B
¬
F A
B
1
¬
F A
1
-
¬
F A
¬
F A
B
Ù
¬
F A
B
Ú
¬
F A
B
¬
F
A
¬
F B
¬
F
sr
B
¬
F
sl
B
¬
+
+
+
+
+
+
Å

## Slide 37: Microoperations for the Datapath - Symbolic Representation
Micr
o-
op
eratio
n
D
A
A
A
B
A
M
B
F
S
M
D
R
W
R
1
R
2
R
3
R
e
g
ister
F
unction
Write
R
4
—
R
6
R
e
g
ister
F
unction
Write
R
7
R
7
—
Re
gister
Function
Write
R
1
R
0
—
Con
s
tant
Func
tio
n
Write
——
R
3
R
eg
i
s
t
e
r
—
—
N
o Wr
it
e
R
4
——
—
—
Data in
Write
R
5
R
0
R
0
R
e
g
ister
F
unction
Write
R
1
R
2
R
3
–
¬
F A
B
1
+ +
=
R
4
s
l R6
¬
F
sl
B
=
R
7
R
7 1
+
¬
F A
1
+
=
R
1
R
0 2
+
¬
F A
B
+
=
Data out
R
3
¬
R
4
D
ata in
¬
R
5 0
¬
F A
B
Å
=

## Slide 38: Microoperations for the Datapath - Binary Representation
m
Microoperations from T
a
Binary C
o
o
Results of simulation of the above on the next slide
Micr
o-
o
p
eratio
n
D
A
A
A
B
A
M
B
F
S
M
D
R
W
0
0
1
0
1
0
011
0
010
1
0
1
10
0
XX
X
110
0
111
0
0
1
11
1
1
11
XXX
0
000
1
0
1
00
1
0
00
XXX
1
001
0
0
1
XX
X
X
XX
011
0
XXX
X
X
0
10
0
XX
X
XXX
X
XXX
X
1 1
1
0
1
0
0
0
000
0
101
0
0
1
R
1
R
2
R
3
–
¬
R
4
s
l R6
¬
R
7
R
7 1
+
¬
R
1
R
0 2
+
¬
Data out
R
3
¬
R
4
D
ata in
¬
R
5 0
¬

## Slide 39: Datapath Simulation

## Slide 40: Terms of Use
All (or portions) of this material © 2008 by Pearson Education, Inc.
Permission is given to incorporate this material or adaptations thereof into classroom presentations and handouts to instructors in courses adopting the latest edition of Logic and Computer Design Fundamentals as the course textbook.
These materials or adaptations thereof are not to be sold or otherwise offered for consideration.
This Terms of Use slide or page is to be included within the original materials or any adaptations thereof.